## Slide 1: Energy Saving Guide
How much in Energy Savings are you missing out on?
Where can more energy be saved with simple changes?
What low cost changes will be a good return on investment?
Presented By Matthew Bulat
M.Eng.Tech
http://www.matthewb.id.au/

## Slide 2: Saving Categories Sample
Lighting
Hot Water
Cooling
Heating
Entertainment
Computers
Appliances
Timers
Measurement

## Slide 3: Lighting
Change light bulbs for compact fluorescent lights or LED lights to save 80-88% on electricity.
Use fluorescent tubes with electronic controllers (ballasts) with lower wattage tubes and save 33%.
Consider replacing halogen light fittings for compact fluorescent lights that fit in the same area.
Use sunlight instead of artificial light if available.
Turn off lights when you leave a room.

## Slide 5: Year Running Cost for 2hrs/day
Old Light | Efficient Light | Old Light Costs | New Light Costs | Savings per year
Incandescent 60W | Compact Fluorescent 13 W | $7.01 | $1.28 | $5.72
PAR 38 Floodlight 125 W | PAR 38 CFL 23 W | $14.60 | $2.69 | $11.91
Halogen Downlight 55 W | CFL Downlight 13 W | $6.42 | $1.52 | $4.91
Fluorescent Magnetic 36 W | Fluorescent Electronic 24 W | $4.20 | $2.80 | $1.40
Power Value used $0.16 / kWh. Efficient light also have less replacement requirements.
To work out your exact savings for your lighting hours see Light Energy Calculator

## Slide 6: Hot Water
Install water saving shower rose and tap aerators to save over 50% on hot water.
Try to limit showers to 4 minutes to save on hot water. Timers are available.
Fix any water leaks promptly. They can add 20000 litres per year to your usage.
Work out how much hot water you use per year and see if solar hot water is cost effective. See Solar Hot Water Calculator and possibly save 80% in hot water power consumption.

## Slide 8: Sample Hot Water Yearly Running Costs
Water Use per Day | Quantity | Units
Showers | 12 | minutes
Taps | 5 | minutes
Dishwasher | 1 | use
Bath | 1 | fill
Water Results per year | Regular fittings | Efficient Fittings | Savings per year
Water consumption litres | 82125 | 44347 | 37778
Power Used kWh | 4271 | 2306 | 1965
Power Cost @ $0.16/kWh | 683 | 369 | 314
To work out your exact savings for your hot water use see Hot Water Calculator

## Slide 9: Cooling and Heating
Cooling and heating consumes approximately 40% of the household energy budget in Australia.
Insulation of walls and ceiling can reduce this running cost and cooling/heating capital costs.
Glass tinting can reduce 80% of solar radiation.
Roof ventilation can reduce loft temperature by 5 degrees.
Reducing electrical loads also reduces cooling requirements.
Consider running some air conditioners on off peak power to save in running costs.
Clean air conditioner filter regularly to maintain efficiency.
Control the area cooled or heated by closing doors, windows and stopping drafts
Reverse cycle heating is about 3 times more efficient than resistive heaters.

## Slide 10: Sample Heating Cooling Savings
Year Power Cost $ | 40% Heating Cooling Cost $ | 25% saving per year | 50% saving per year | 75% saving per year
500 | 200 | 50 | 100 | 150
1000 | 400 | 100 | 200 | 300
1500 | 600 | 150 | 300 | 450
2000 | 800 | 200 | 400 | 600
2500 | 1000 | 250 | 500 | 750
3000 | 1200 | 300 | 600 | 900

## Slide 11: Entertainment
Consider placing a rooms entertainment equipment on one power board and switching it off at the wall when not in use.
Appliances can be controlled by remote controlled power boards if power point access is difficult.
Turn off gaming consoles at the wall when not in use and save up to $200 per year.
Look for 1 watt standby appliances.

## Slide 12: Sample Entertainment Equipment Standby Costs
Appliance | Standby Watts | Year Standby Cost @ $0.16/kWh | Potential Savings if off at wall when not in use
DVD Player | 20 | $27.19 | $27
Wii | 2 | $2.72 | $3
Xbox 360 | 140 | $190.31 | $190
PS3 | 190 | $258.28 | $258
TV poor | 20 | $27.19 | $27
TV best | 1 | $1.36 | $1
To work out your exact savings for your appliances see Appliance Energy Calculator

## Slide 13: Computers
Turn on computer power management with screen power down at 15 minutes and computer sleep in 30 minutes of inactivity.
Control computer peripherals with a USB controlled power board that is only on when the computer is on.
Choose a laptop instead of a desktop and save over 50% in energy costs on average.
Buy computers with Energy Star 4 or 5 rating and include 80 Plus standard power supplies (> 80% efficient)

## Slide 14: Sample Computer Saving Choices
Computer Type | Year Power Used for 45 hours / week in kWh | Year Power Cost @ $0.16/kWh | Savings
Un-optimized Dual Core Desktop | 503 | $80 | 
Energy Star 4 Desktop | 239 | $38 | $42
Energy Star 4 Laptop | 109 | $17 | $63
Netbook | 37 | $6 | $74
To work out your exact savings for your computers see Computer Energy Calculator
If building an efficient computer see Computer Power Consumption Calculator

## Slide 15: Appliances
Use cold water for the washing machine. Save 50 - 150 litres of hot water costs per load.
Use clothes line rather than dryer. Save about $100 per year.
Turn off fridges that do not need to be in use. Save about $100 for each fridge turned off per year.
Look for new appliances with 1 watt standby and are top performers in Energy Stars.

## Slide 16: Timers
Consider daily, weekly, countdown timers or sensors to limit lighting hours.
Countdown timers can be used for classrooms, stairways, walkways, exhaust fans etc.
Run pool pumps on timers and vary run time relative to seasonal needs.
Any device with a moderate standby power consumption may benefit from a timer.

## Slide 17: Electricity Measurement
Consider measuring electricity consumption to accurately measure savings. Actively try to keep a lower average consumption.
$25 for power point measurement.
$100 for building power measurement.
$150 for large building 3 phase power measurement.
Home Energy Monitoring Building Energy Monitoring

## Slide 18: Energy Saving Tips Conclusion
Which tips seem most attractive to you?
Research the costs and savings online.
Make a priority list of easiest or cheapest changes to implement.
Try to measure the before and after effects of the efficiency change to work out how much you save year after year.
Start saving $100s or $1000s every year.
For more information see http://www.matthewb.id.au/